## Slide 2: Saks & Associates
393 Leander Dr.
Springfield, OH 45504-4906 USA
+1-937-324-3601 (voice)
ben@saksandassociates.com
www.saksandassociates.com

## Slide 3: About Ben Saks
Ben Saks is the chief engineer of Saks & Associates. He is the principal editor and presenter for much of Saks & Associates’ training curriculum on the use of C and C++ in embedded systems.
Ben represents Saks & Associates on the ISO C++ Standards committee as well as two of the committee’s study groups:
        SG14 — low-latency
        SG20 — education
Ben has spoken at industry conferences, including CppCon: The C++ Conference, the C++ and System Software Summit, the Embedded Systems Conference, and NDC Techtown. He’s been the chair of the Embedded Track at CppCon since 2020, and is also on CppCon’s program committee.

## Slide 4: More About Ben Saks
Ben previously worked as a software engineer for Vorne Industries, where he used C++ and JavaScript to develop embedded systems that help improve manufacturing productivity in factories all over the world. He is a contributing author on multiple Vorne patents.
Ben earned a B.A. with Distinction in Computer Science from Carleton College.

## Slide 5: About Dan Saks
Dan Saks is the president of Saks & Associates, which offers training and consulting in C and C++ and their use in developing embedded systems.
Dan used to write the “Programming Pointers” column for embedded.com online. He also wrote columns for numerous print publications (when such things existed) including The C/C++ Users Journal, The C++ Report, Software Development, and Embedded Systems Design. With Thomas Plum, he wrote C++ Programming Guidelines, which won a 1992 Computer Language Magazine Productivity Award.
Dan has taught C and C++ to thousands of programmers around the world. He has delivered hundreds of lectures, including a few keynote addresses, at conferences such as the ACCU (Association of C and C++ Users) Conference, code::dive, CppCon: The C++ Conference, the Embedded Systems Conference, Meeting Embedded, and NDC Techtown.

## Slide 6: More About Dan Saks
Dan served as secretary of the ANSI and ISO C++ Standards committees and as a member of the ANSI C Standards committee. He also contributed to the CERT Secure C Coding Standard and the CERT Secure C++ Coding Standard.
Dan collaborated with Thomas Plum in writing and maintaining Suite++™, the Plum Hall Validation Suite for C++, which tests C++ compilers for conformance with the international standard. He was a Senior Software Engineer for Fischer and Porter (now ABB), where he designed languages and tools for distributed process control. He also worked as a programmer with Sperry Univac (now Unisys).
Dan earned an M.S.E. in Computer Science from the University of Pennsylvania, and a B.S. with Highest Honors in Mathematics/ Information Science from Case Western Reserve University.

## Slide 7: Overview
Embedded applications are generally written for specific hardware.
        Obviously, our application needs to work on that target hardware.
However, developing on real hardware isn’t always ideal – it carries certain costs.
        For one thing, it takes time to upload code to the hardware.
        Using real hardware also limits our ability to test and debug the code (e.g., we might need a hardware debugger).
We can minimize the impact of these costs on development if we can also run (most of) our application in a simulated environment.

## Slide 8: Overview
We’ll examine a simple program that runs on the ARM Evaluator 7-T (E7T).
The example program:
        reads data from a serial port (UART), one character at a time, and
        displays that character on a 7-segment display.
Then we’ll make the same main program run on a simple simulation of that hardware as a traditional application.
        In both versions, the program’s code will be identical down to the level of using individual hardware registers.
        We’ll use operator overloading to make the simulated registers behave similarly to the target hardware registers.

## Slide 9: The ARM Evaluator-7T
7-segment display
user serial port (COM0)
debug serial port (COM1)

## Slide 10: Our Example Program
Our example program uses two objects representing hardware devices:
        uart0, a pointer to a UART object that represents a serial port, and
        display, a pointer to an object of type seg7_display.
We’ll focus on simulating the hardware for UART 0.
        However, the simulated 7-segment display uses the same techniques.

## Slide 11: Our Example Program
Here is most of our example program:
      int main() {
      // object definitions for uart0 and display
      for (;;) {
      char c;
      if (uart0->get(c)) {
      display->put(c);
      }
      }
      }
We’ll look at how to create uart0 and display in a moment.

## Slide 12: Our Example Program
uart0->get(c) attempts to read a character from UART 0 into c.
        It’s modeled on std::istream::get(char &c).
        If there’s a character to read, it stores the character into c and returns true.
        Otherwise, it returns false.
display->put(c) displays the character c on the 7-segment display.
        A 7-segment display can’t quite display the entire English alphabet, but it can get pretty close.

## Slide 13: Classes and Memory-Mapped Hardware
There are many ways to write class interfaces for hardware devices.
These slides use a variation of the techniques described in CppCon 2020’s Memory-Mapped Devices as Objects by Dan Saks. [CppCon 2020]
This session focuses on using operator overloading to create simulated hardware registers that behave much like real hardware registers.
You can adapt these techniques to other ways of writing class interfaces for hardware devices.

## Slide 14: Memory-Mapped Hardware
First, we’ll focus on how to create uart0 and display for the target hardware.
CPUs typically communicate with external devices via device registers.
        A device register is circuitry that provides an interface to a device.
Like most modern hardware, the E7T uses memory-mapped device registers.
        That is, the hardware assigns each device register an address in the memory space.

## Slide 15: “Typical” Address Space
A “typical” address space with memory-mapped registers looks like:
    interrupt vectors
    physical memory (RAM, ROM, Flash)
    memory-mapped registers
    ______________________ _______________
    lowest address (=0) base address

## Slide 16: Memory-Mapped Hardware
In C++, you can access a memory-mapped register as if it was an ordinary object via an appropriately-initialized pointer, such as:
      using device_register = std::uint32_t volatile;
      device_register *const ULCON {
      reinterpret_cast<device_register *>)(0x03FFD000)
      };
Alternatively, you can use a reference:
      device_register &ULCON {
      *reinterpret_cast<device_register *>)(0x03FFD000)
      };

## Slide 17: Devices with Multiple Registers
Many hardware devices have multiple registers, often located at contiguous addresses.
For example, the E7T has two serial ports (UARTs), each with the same layout:
Offset | Register | Description
0x00 (0) | ULCON | line control
0x04 (4) | UCON | control
0x08 (8) | USTAT | status
0x0C (12) | UTXBUF | transmit buffer
0x10 (16) | URXBUF | receive buffer
0x14 (20) | UBRDIV | baud rate divisor (control)

## Slide 18: A UART Class
Rather than access a UART’s device registers individually, we can group them together into a UART class:
      class UART {
      public:
      enum baud_rate { BR_9600 = 162 << 4, ~~~ };
      UART(baud_rate br);
      bool get(char &c);
      ~~~
      private:
      device_register ULCON;
      device_register UCON;
      device_register USTAT;
      ~~~
      };

## Slide 19: The UART Constructor
UART’s constructor:
        ensures that the UART is disabled (i.e., can’t transmit or receive),
        sets the baud rate, and then
        enables the UART for both transmitting and receiving.
      constexpr std::uint32_t UART::RXM {1};
      constexpr std::uint32_t UART::TXM {8};
      UART::UART(baud_rate br) {
      UCON = 0;
      UBRDIV = br;
      UCON = RXM | TXM;
      }

## Slide 20: The UART Constructor
We can make this constructor more maintainable by using inline functions such as disable and enable:
      UART::UART(baud_rate br) {
      disable();
      UBRDIV = br;
      enable();
      }
      inline void UART::disable() { UCON = 0; }
      inline void UART::enable() { UCON = RXM | TXM; }

## Slide 21: Reading from a UART
Hardware operations often involve multiple hardware registers.
For example, when an external system transmits data to one of the E7T’s UARTs, it’s stored in the UART’s URXBUF register, one character at a time.
Upon receiving a character, the UART sets the Receive Data Ready (RDR) bit in the USTAT register.
We should read from URXBUF only when the RDR bit is set.
        Reading from URXBUF automatically clears the RDR bit in USTAT.

## Slide 22: Reading from a UART
Here’s the body of UART::get with the hardware registers highlighted:
      constexpr std::uint32_t UART::RDR {0x20};
      bool UART::get(char &c) {
      if ((USTAT & RDR) == 0) {
      return false;
      }
      c = static_cast<char>(URXBUF);
      return true;
      }
While UART::get isn’t that complex, it’s easy to imagine similar code that does real significant work.

## Slide 23: Setting Up for the Target Hardware
UART 0’s registers are located at specific memory-mapped addresses chosen by the hardware.
On the target hardware, functions like UART::get will work correctly only if the UART’s data members are located at those memory addresses.
We need to position the UART object accordingly.
        We’ll do that using a special form of new.
        One that doesn’t allocate memory.

## Slide 24: New-Expressions
A typical new-expression has the form:
      p = new T (v); // or {v} in Modern C++
It translates into something (sort of) like:
      p = static_cast<T *>(operator new(sizeof(T)));
      p->T(v);
Here, p->T(v) means “apply to *p the T constructor that accepts argument v”.
        It’s not real C++.

## Slide 25: Class-Specific New
C++ lets you declare operator new as a class member.
If T is a class with a member operator new, then this uses T’s operator new:
      p = new T (v); // or {v} in Modern C++
It translates into something (sort of) like:
      p = static_cast<T *>(T::operator new(sizeof(T)));
      p->T(v); // again, this isn't real C++
New-expressions for all other types continue to use the global operator new.

## Slide 26: Class-Specific New
A class-specific T’s operator new need not return memory from the free store.
On the target platform, UART’s operator new always returns UART 0’s memory-mapped address:
      class UART {
      public:
      void *operator new(std::size_t) {
      return reinterpret_cast<void *>(address);
      }
      ~~~
      private:
      static constexpr uintptr_t address = 0x03FFD000;
      ~~~
      };

## Slide 27: Class-Specific New
seg7_display has a similar class-specific operator new.
On the target platform, it always returns the 7-segment display’s memory-mapped address:
      class seg7_display {
      public:
      void *operator new(std::size_t) {
      return reinterpret_cast<void *>(address);
      }
      ~~~
      private:
      static constexpr uintptr_t address = 0x03FF5000;
      ~~~
      };

## Slide 28: Class-Specific New
A class T with a member operator new should also have a member operator delete.
        Otherwise, deleting a T will invoke the global operator delete.
Since these class-specific operator news don’t actually allocate memory, the class-specific operator deletes have nothing to do:
      class UART {
      public:
      void *operator new(std::size_t) { ~~~ }
      void operator delete(void *) { }
      ~~~
      };

## Slide 29: Creating uart0 and display
With these class-specific operator news in place, we can create uart0 and display with simple new-expressions:
      int main() {
      UART *uart0 = new UART;
      seg7_display *display = new display;
      for (;;) {
      char c;
      if (uart0->get(c)) {
      display->put(c);
      }
      }
      }

## Slide 30: Challenges of Real Hardware
Our program will now run correctly on our target hardware.
However, developing on real hardware isn’t always practical or convenient:
        The target hardware might still be under development (e.g., if the project is still in its early stages).
        It takes time to upload the compiled program to the target hardware.
        It’s difficult to test error recovery code on the target hardware because we can’t reliably make the hardware fail.
How can we simulate the hardware and run essentially the same code in a desktop environment?

## Slide 31: First Attempt at a Simulator
Our current versions of the UART and seg7_display classes implement their interfaces in terms of the target hardware.
Running just the main program in a simulated environment is easy.
        We simply write new versions of UART and seg7_display that implement those interfaces differently.

## Slide 32: A Simulated UART Class
For example, here’s a simulated version of the UART class that reads characters from a file:
      class sim_UART {
      public:
      enum baud_rate { BR_9600 = 162 << 4, ~~~ };
      UART(baud_rate br);
      bool get(char &c);
      ~~~
      private:
      std::ifstream file;
      };

## Slide 33: Reading from a Simulated UART
The body of sim_UART::get is simply:
      bool sim_UART::get(char &c) {
      return file.get(c);
      }
As a simulator for just the main program, this works fine.

## Slide 34: Simulating at a Lower Level
However, as we saw earlier, the original UART::get is non-trivial:
      bool UART::get(char &c) {
      if ((USTAT & RDR) == 0) {
      return false;
      }
      c = static_cast<char>(URXBUF);
      return true;
      }
Can we write our simulation so that it can also run this code?

## Slide 35: Simulating at a Lower Level
In other words, we want to get our UART class (or something very close to it) running in our simulation:
      class UART {
      public:
      enum baud_rate { BR_9600 = 162 << 4, ~~~ };
      UART(baud_rate br);
      bool get(char &c);
      ~~~
      private:
      device_register ULCON;
      device_register UCON;
      device_register USTAT;
      ~~~
      };

## Slide 36: Simulating Individual Registers
On the target hardware, there are side effects to accessing hardware registers.
For example, reading from URXBUF clears the RDR flag in USTAT.
      class UART {
      ~~~
      private:
      device_register ULCON;
      device_register UCON;
      device_register USTAT;
      ~~~
      };
Our simulation should produce similar side effects when accessing these device_register members.

## Slide 37: Simulating Individual Registers
More specifically, our device_register objects will need to support two different side effects:
        An on-read side effect (e.g., so reading from URXBUF can alter the state of USTAT).
        An on-write side effect (e.g., so we can take the appropriate actions to enable or disable the UART when writing to UCON).
Moreover, different device_registers might need to have different side effects.

## Slide 38: Simulating Individual Registers
On the target hardware, device_register was a type alias:
      using device_register = std::uint32_t volatile;
In our simulation, device_register will be a class type that contains a single non-static data member of a similar type:
      class device_register {
      public:
      ~~~
      private:
      std::uint32_t volatile value;
      ~~~
      };

## Slide 39: The device_register Class
UART::get reads from device_registers as if they were std::uint32_ts:
      bool UART::get(char &c) {
      if ((USTAT & RDR) == 0) {
      return false;
      }
      c = static_cast<char>(URXBUF);
      return true;
      }
This worked on the target hardware because device_register was a type alias for std::uint32_t volatile.
        How can we make it work in the simulation?

## Slide 40: The device_register Class
A conversion operator defines an implicit conversion from a user-defined type to another type.
        It returns an object of the converted-to type.
Here, it also provides a place to insert the code for the on-read side effect:
      class device_register {
      public:
      operator std::uint32_t() {
      // trigger on-read side effect
      return value;
      }
      ~~~
      };

## Slide 41: The device_register Class
With the conversion operator, UART::get behaves as if it were written:
      bool UART::get(char &c) {
      if ((USTAT.operator std::uint32_t() & RDR) == 0) {
      return false;
      }
      c = static_cast<char>(URXBUF.operator std::uint32_t());
      return true;
      }

## Slide 42: The device_register Class
Similarly, UART::disable and UART::enable write to a device_register as if it were a std::uint32_t:
      inline void UART::disable() { UCON = 0; }
      inline void UART::enable() { UCON = RXM | TXM; }
We can get the desired behavior by overloading operator= for device_register…

## Slide 43: The device_register Class
device_register::operator= will trigger the on-write side effect:
      class device_register {
      public:
      void operator=(std::uint32_t v) {
      value = v;
      // trigger on-write side effect
      }
      ~~~
      };
Ordinarily, operator= returns a reference to the target object.
        Here, it returns void so it can’t be used to read from the register.

## Slide 44: The device_register Class
device_register also supports the bitwise operations &= and |=.
        Since these involve both reading and writing, they trigger both side effects:
      void device_register::operator&=(std::uint32_t v) {
      // trigger on-read side effect
      value &= v;
      // trigger on-write side effect
      }
      void device_register::operator|=(std::uint32_t v) {
      // trigger on-read side effect
      value |= v;
      // trigger on-write side effect
      }

## Slide 45: Side Effects
Each device_register might need to support different side effects.
Ordinarily, C++ provides many ways to solve this problem.
However, we’re limited by how memory-mapped types like UART declare their device_registers...

## Slide 46: Side Effects
Firstly, UART declares all of its registers as the same type:
      class UART {
      ~~~
      private:
      device_register ULCON;
      device_register UCON;
      device_register USTAT;
      ~~~
      };
As such, we can’t use virtual functions or templates to provide different side effects for different registers.

## Slide 47: Side Effects
Moreover, we want UART to use the same constructor that it uses on the target hardware.
This UART constructor has no member initializers.
        Thus, it default-constructs every one of its device_register members:
      UART::UART(baud_rate br) {
      disable();
      UBRDIV = br;
      enable();
      }
As such, we can’t rely on the constructor to specify the side effect handlers for the device_registers.

## Slide 48: Side Effects by Location
Let’s try basing each register’s side effects on its memory location.
        After all, that’s how it works on the target hardware.
We’ll represent each side effect as a pointer to a function that takes a std::uint32_t (representing the value of the register):
      class device_register {
      public:
      using effect_handler = void (*)(std::uint32_t);
      ~~~
      };
Alternatively, we could use std::function<void(std::uint32_t)> for greater flexibility.

## Slide 49: Side Effects by Location
Each device_register can have an associated effect_handlers object that stores its side-effect handlers:
      class device_register {
      public:
      using effect_handler = void (*)(std::uint32_t);
      struct effect_handlers {
      effect_handler on_read;
      effect_handler on_write;
      };
      ~~~
      };

## Slide 50: An Example Side-Effect Handler
For example, reading from URXBUF should trigger a side effect that clears the RDR bit in the USTAT register.
Therefore, URXBUF’s on-read handler might look something like this:
      void on_URXBUF_read(std:uint32_t v) {
      USTAT &= ~UART::RDR;
      };

## Slide 51: An Example Side-Effect Handler
Once that handler is in place, device_register will invoke it whenever a read occurs using code like this:
      class device_register {
      public:
      operator std::uint32_t() {
      effect_handler on_read = get_read_handler(this);
      if (on_read) {
      on_read(value);
      }
      return value;
      }
      ~~~
      };

## Slide 52: Setting Up Side Effects
device_register will use a static data member of type std::map to associate each device_register’s location with its effect_handlers object:
      class device_register {
      public:
      static void set_register_effects(device_register *reg,
      effect_handlers const &effects) {
      reg_effects[reg] = effects;
      }
      ~~~
      private:
      static std::map<device_register *, effect_handlers> reg_effects;
      ~~~
      };

## Slide 53: Dynamic Memory and Simulations
Often, embedded systems must deal with limitations that might not apply to a traditional application.
        For example, dynamically-allocated memory might not be available.
        This can make it hard to use containers like std::map in embedded systems.
However, this std::map is part of the simulation.
        It’s never used on the target hardware.
        It’s not subject to the same platform-specific limitations.

## Slide 54: Positioning Simulated Registers
For this system to work, we need to place our UART at a fixed memory location.
Fortunately, we’ve already done this using class-specific operator new.
We need to write a different UART::operator new for our simulation that uses an appropriate location…

## Slide 55: Positioning Simulated Registers
As we’ll see, there are a number of pieces to the simulated UART.
We can separate them from the main UART code by putting them in a base class called basic_sim_UART…

## Slide 56: Positioning Simulated Registers
      class basic_sim_UART {
      public:
      void *operator new(std::size_t);
      void operator delete(void *);
      };
      class UART: public basic_sim_UART {
      public:
      using basic_sim_UART::operator new;
      using basic_sim_UART::operator delete;
      ~~~
      };

## Slide 57: Isolating Target vs. Simulation Differences
Similarly, we can put the code specific to the target hardware in a base class called basic_E7T_UART…

## Slide 58: Isolating Target vs. Simulation Differences
      class basic_E7T_UART {
      public:
      void *operator new(std::size_t);
      void operator delete(void *);
      ~~~
      };
      class UART: public basic_E7T_UART {
      public:
      using basic_sim_UART::operator new;
      using basic_sim_UART::operator delete;
      ~~~
      };

## Slide 59: Isolating Target vs. Simulation Differences
With a little conditional compilation, we can use the main UART class for both the target hardware and the simulation:
      #ifdef SIMULATING
      class basic_sim_UART { ~~~ };
      using basic_UART = basic_sim_UART;
      #else
      class basic_E7T_UART { ~~~ };
      using basic_UART = basic_E7T_UART;
      #endif
      class UART: public basic_UART { ~~~ };

## Slide 60: Positioning Simulated Registers
Returning to basic_sim_UART, we’ll add two static data members:
        sim_hardware, the memory where we’ll construct the UART, and
        sim_handlers, containing the side-effect handlers associated with each device_register.
      class basic_sim_UART {
      public:
      void *operator new(std::size_t);
      void operator delete(void *);
      private:
      static device_register sim_hardware[6];
      static device_register::effect_handlers const sim_handlers[6];
      };

## Slide 61
In addition to positioning the object, basic_sim_UART:operator new will set up the side-effect handlers for each register:
      class basic_sim_UART {
      void *operator new(std::size_t) {
      for (int i = 0; i < std::ssize(sim_hardware); ++i) {
      device_register::register_effects(&sim_hardware[i],
      sim_handlers[i]);
      }
      return reinterpret_cast<void *>(sim_hardware);
      }
      ~~~
      private:
      static device_register sim_hardware[6];
      static device_register::effect_handlers const sim_handlers[6];
      };

## Slide 62: Creating Side Effects
We can implement each side-effect handler as a private static member function of basic_sim_UART:
      class basic_sim_UART {
      public:
      void *operator new(std::size_t);
      void operator delete(void *);
      private:
      static device_register sim_hardware[6];
      static device_register::effect_handlers const sim_handlers[6];
      static void on_sim_URXBUF_read(std:uint32_t v);
      static void on_sim_UCON_write(std::uint32_t v);
      };

## Slide 63: Creating Side Effects
We specify the appropriate handlers when we define the sim_handlers array:
      device_register::effect_handlers const
      basic_sim_UART::sim_handlers[6] =
      {
      {},
      {nullptr, on_sim_UCON_write},
      {},
      {},
      {on_sim_URXBUF_read, nullptr},
      {}
      };

## Slide 64: Creating Side Effects
As private static member functions, our side-effect handlers can access the registers as static data members of basic_sim_UART.
Here’s a revised attempt at the side-effect handler for reading from URXBUF:
      void basic_sim_UART::on_sim_URXBUF_read(std:uint32_t v) {
      device_register &sim_USTAT = sim_hardware[2];
      sim_USTAT &= ~UART::RDR;
      };

## Slide 65: Creating Side Effects
Unfortunately, we’ve done our job too well.
Since sim_USTAT is a device_register object, this line will trigger the side effects for reading and writing:
      void basic_sim_UART::on_sim_URXBUF_read(std:uint32_t v) {
      device_register &sim_USTAT = sim_hardware[2];
      sim_USTAT &= ~UART::RDR;
      };
Our side-effect handlers need a way to read from and write to device_registers without triggering more side effects.

## Slide 66: Opening a Backdoor
We can add member functions to device_register to do this:
      class device_register {
      public:
      std::uint32_t backdoor_read() const { return value; }
      void backdoor_write(std::uint32_t v) { value = v; }
      void backdoor_bit_and(std::uint32_t v) { value &= v; }
      void backdoor_bit_or(std::uint32_t v) { value |= v; }
      ~~~
      };
However, we probably don’t want these functions to be available to the whole application…

## Slide 67: Opening a Backdoor
As an alternative, we can make them protected members of device_register…
      class device_register {
      protected:
      std::uint32_t backdoor_read() const { return value; }
      void backdoor_write(std::uint32_t v) { value = v; }
      void backdoor_bit_and(std::uint32_t v) { value &= v; }
      void backdoor_bit_or(std::uint32_t v) { value |= v; }
      ~~~
      };

## Slide 68: Opening a Backdoor
Then we can make these members accessible only through a derived class, sim_device_register…
      class sim_device_register: public device_register {
      public:
      using device_register::backdoor_read;
      using device_register::backdoor_write;
      using device_register::backdoor_bit_and;
      using device_register::backdoor_bit_or;
      };
      static_assert(
      is_layout_compatible_v<sim_device_register, device_register>,
      "Ensure layout compatibility of device_register types");

## Slide 69: Opening a Backdoor
… and use sim_device_register in basic_sim_UART instead:
      class basic_sim_UART {
      public:
      ~~~
      private:
      static sim_device_register sim_hardware[6];
      static device_register::effect_handlers const sim_handlers[6];
      ~~~
      };

## Slide 70: Opening a Backdoor
Now our side-effect handlers can use these backdoors…
      void basic_sim_UART::on_sim_URXBUF_read(std:uint32_t v) {
      sim_device_register &sim_USTAT = sim_hardware[2];
      sim_USTAT.backdoor_bit_and(~UART::RDR);
      };

## Slide 71: Opening a Backdoor
…while code in UART and elsewhere sees plain device_registers with no backdoors:
      class UART: public basic_UART {
      ~~~
      private:
      device_register ULCON;
      device_register UCON;
      device_register USTAT;
      ~~~
      };
This is valid if device_register and sim_device_register are layout-compatible.

## Slide 72
Now we’re free to write whatever side-effect handlers our simulation needs.
For example, when the UART is enabled, this handler spawns a thread that simulates receiving 100 'A' characters, one per second:
      void basic_sim_UART::on_sim_UCON_write(std::uint32_t v) {
      if (v == (UART::RXM | UART::TXM)) {
      static std::thread producer_thread([]() {
      for (int i = 0; i < 100; ++i) {
      std::this_thread::sleep_for(1000ms);
      sim_URXBUF.backdoor_write('A');
      sim_USTAT.backdoor_bit_or(UART::RDR);
      }
      });
      producer_thread.detach();
      }
      }

## Slide 73: The End
Thanks for Listening

## Slide 74: Bibliography
CppCon. (2020, Oct 7). Memory-Mapped Devices as Objects - Dan Saks - CppCon 2020 [Video]. YouTube. https://youtu.be/uwzuAGtAEFk